FieldBus19

White Paper

Version:	1.00

Last Edit:	December 6, 2021

Author:	Andreas Isenegger

Filename:	FB19_WhitePaper.odt

Document Revision History

Version	Date	Author	Changes

1.00	06-Dec-2021	A. Isenegger	Initial version

Table 1: Document revision history

# Introduction
## Purpose of this Document
This document stores the basic goals of a to be developed field bus called FieldBus19.
It also provides an overview of existing field bus specifications and details the next steps towards the implementation of an initial proof of concept FieldBus19 prototype.
## History
The ideas to this project came up years ago, but I didn’t put down initial notes until the fall of 2019 when I was on a bike holiday in the Tuscany, one of the most beautiful parts of Italy. It seemed to me that the embedded systems community still lacked a self-configuring, light-weight, simple to use, operating system and vendor independent, open source field bus.
## Purpose of the Project
The purpose of the FieldBus19 project is to simplify the interconnection of micro-controller boards that have relatively little CPU and memory resources. This task is simple and has been solved in many good ways when it comes to hardware and the lower software levels. The medium to highest OSI layers however are poorly covered by existing libraries, if there exist any apart from UDP, TCP/IP and the like.
In contrast to a CAN bus network – to give one example – the FieldBus19 covers higher OSI layers than CAN does and arbitrates bus access in a different, more easily controllable manner, thereby showing fully deterministic behavior.

# Goals
## Functional Goals
- Deterministic
  During normal operation, the exchange of information shall be 100 percent deterministic (predictable in size and time). Only during mechanical or electrical fault states and during the bus initialization phase data exchange might be stochastic (non-predictable).
- Automatic node address assignment
  The addition or removal of network nodes shall be automatically detected by the software. It shall not require DIL switch settings or hard-coded values for defining a node’s bus address.
- Locked or unlocked list of bus participants
  For supporting product development and yet not compromising safety during productive operation, the bus shall support two modes, ‘unlocked’ and ‘locked’. In ‘unlocked’ mode, nodes are added and removed automatically as they appear and disappear on the bus line. In ‘locked’ mode, the number of nodes and their addresses is fix. New nodes won’t be included in the communication exchange, and removed nodes will be noted as missing. If they come back, communication shall be re-established.
- Programmable bit rate
  Depending on the domain application, 1kbit/s may be as adequate as 10Mbit/s. During the run-time of a bus and its connected nodes the bit rate shall remain constant.
- Variable packet size
  Packets that can be adapted to the data size they carry result in a higher bus transfer data rate efficiency. Thus, packets shall be variable in size within a certain range.
- CRC protected data
  While on the bus line, the data packets shall be protected against corruption by a CRC sum.
- Optionally redundant
  The FieldBus19 system shall have the capability of optionally being operated with redundant nodes, connectors and cables.
## Non-functional Goals
- Well documented
  The project and its code shall come with adequate documentation, including its specifications, explanations and examples. Videos for user initial guidance is also considered part of the documentation.
- Simple hardware requirements
  The FieldBus19 software shall be implemented using UARTs and timers. No additional hardware shall be required, neither internally nor externally to the micro-controller. The use of DMA or external safety logic is optional.
- Operating system independent
  Neither the drivers nor the higher software layers of the FieldBus19 library shall depend on a specific real-time kernel or operating system. They may be used however in the context of and by a real-time kernel, or they may run on ‘bare metal’ either.
- Static memory resource allocation
  For safety reasons and for saving processor resources, the libraries shall allocate RAM statically only.
- Light weight
  The CPU, RAM and ROM overhead for using this bus shall be small and also fit micro-controllers that have little resources.
- Simple to use
  It is simple to interconnect a few RS-485 transceivers, and it shall also be simple to hook the FieldBus19 libraries into a domain specific application. Ideally their API is simple enough that also hobby programmers can make use of them.
- Royalty free
  There shall be no charges of any kind for using this bus system.
- Open source
  The source code of all hard- and software parts of the FieldBus19 system shall be open to the public, hosted on a public code repository. Applications that make use of this field bus system may be closed source.
## Excluded Goals
Intentionally excluded from the goals and specifications are:
- Minimum, standard or maximum bit rates
- Connectors
- Cables
- Mechanical form factors of any kind
- Electrical specifications of any kind; some recommendations will be provided

# Existing Bus Systems
Many of nowadays micro-controllers have enough CPU and memory resources that applications can use UDP or TCP/IP via (W)LAN for exchanging information between each other, but there is yet a variety of applications where the use of these protocol stacks isn’t possible or not desirable. The FieldBus19 focuses on the latter type of applications.
A few of today’s field bus systems are listed below in alphabetic order. The choice is arbitrary.
Instead of listing all their properties and features, just their less favorable aspects or missing features are listed. Italic text are quotes of external sources, ‘standard text’ comes from this document’s author.
## ARCNET
Source: Wikipedia
ARCNET was developed in the 1970s at Datapoint corporation and became popular in the 1980s for office automation tasks.
Ethernet running TCP/IP protocol stacks eventually won the race. The bus system isn’t in use anymore, thus controller/driver chips are unavailable nowadays.
## ARINC 429
Source: Wikipedia
ARINC 429, "Mark33 Digital Information Transfer System (DITS)," is also known as the Aeronautical Radio INC. (ARINC) technical standard for the predominant avionics data bus used on most higher-end commercial and transport aircraft. It defines the physical and electrical interfaces of a two-wire data bus and a data protocol to support an aircraft's avionics local area network.
It’s a rather old and slow bus system, the data rates are specified as either 12.5kbit/s or 100kbit/s, and it supports only 1 transmitter per single wire pair. The packet length is fixed to 32bit/packet, which is called a ‘word’. It’s protocol doesn’t seem to be widely known.
There are successors of this standard, for example ARINC 629 or ARINC 664.7 (bases on Ethernet), but they contradict the imagination of being simple and light-weight to use.
The MIL-STD-1533B is also similar to ARINC 429. It has interesting concepts, but it doesn’t support what the FieldBus19 project tries to achieve.
## CAN
Source: Wikipedia
In the industrial and automotive environment, the CAN bus is of wide use. This alone is a big advantage, and it has many more. It contains some elegant properties and comes in a variety of ‘add-on’ specifications that make it faster and more secure than its initial version from the eighties. The downside to this is that it can become quite complex to let half a dozen nodes in a CAN environment talk to each other. I’m not speaking about the complexity of the domain application, but the communication modules inside the nodes that make the nodes talk to each other. In addition, either micro-controller internal SoC modules that ‘talk CAN’ or external ICs that convert for example SPI data packets back and forth to CAN are required.
## LIN
Source: Wikipedia
LIN (Local Interconnect Network) is a serial network protocol used for communication between components in vehicles. It is a single wire, serial network protocol that supports communications up to 19.2 Kbit/s at a bus length of 40 meters. The need for a cheap serial network arose as the technologies and the facilities implemented in the car grew, while the CAN bus was too expensive to implement for every component in the car. European car manufacturers started using different serial communication technologies, which led to compatibility problems.
In the late 1990s, the LIN Consortium was founded by five automakers (BMW, Volkswagen Group, Audi, Volvo Cars, Mercedes-Benz), with the technologies supplied (networking and hardware expertise) from Volcano Automotive Group and Motorola. The first fully implemented version of the new LIN specification (LIN version 1.3) was published in November 2002. In September 2003, version 2.0 was introduced to expand capabilities and make provisions for additional diagnostics features. LIN may be used also over the vehicle's battery power-line with a special LIN over DC power line (DC-LIN) transceiver.
The specifications of this bus systems narrow its use to few applications.
## Modbus
Source: Wikipedia
Modbus is a data communications protocol originally published by Modicon (now Schneider Electric) in 1979 for use with its programmable logic controllers (PLCs). Modbus has become a de facto standard communication protocol and is now a commonly available means of connecting industrial electronic devices.
Modbus comes with a variety of different protocol versions (or types) for different applications and transport layers. Several frame formats exist, like ‘RTU’ and ‘ASCII’ for serial data lines like RS-485, or ‘TCP’ for Ethernet networks.
Although some frame formats and also other properties look similar to those of FieldBus19, it is yet quite different when it comes to automatic bus address assignment and the support of higher OSI software layers for example.
Since Modbus was originally intended for use with PLCs, it can address hardware registers directly as its names of object types show (‘coil’, ‘discrete input’, ‘input register’, etc). This makes it look old-fashioned and a bit awkward to use in nowadays applications if correct naming is considered an important part of a product.
## ProfiBus
Source: Wikipedia
Profibus (usually styled as PROFIBUS, as a portmanteau for Process Field Bus) is a standard for fieldbus communication in automation technology and was first promoted in 1989 by BMBF (German department of education and research) and then used by Siemens. It should not be confused with the Profinet standard for Industrial Ethernet. Profibus is openly published as part of IEC 61158.
Profibus networks can run on serial data lines like RS-485, and – depending on the profile – higher OSI layers are supported by the standard. Profiles are pre-defined configurations of the functions and features available from PROFIBUS for use in specific devices or applications.
One downside of this bus system is that it’s various specifications and profiles are maintained by the large PROFIBUS & PROFINET International association, plus the vendors that distribute their products with extensions to the Profibus standard, which is already very broad. This means that although it is promoted as ‘a standard’, devices from different vendors are not fully compatible when it comes to communication, and new products must fit into a profile (or a vendor specific extension of it). All this makes it not very attractive for simple applications.
## RS-232
Source: Wikipedia
This is a hardware specification only. It supports the interconnection of exactly two nodes. This makes it unsuited for interconnecting several micro-controller boards.
## RS-422
Source: Wikipedia
This is a hardware specification only. It does support multiple bus participants, but allows one transmitter per wire pair only, while many receivers are possible. This implies that in a multi-node environment, the bus interfaces and cabling would increase drastically with every transmitting node. This makes it uninteresting for a modern field bus system.
## RS-485
Source: Wikipedia
This is a hardware specification only that supports the interconnection of up to 32 bus participants in half-duplex fashion. Every connected node can be transmitter or receiver, although only one transmitter may be active at any point in time. Since the specification doesn’t support bus arbitration, it has to be programmed into the software of the participating nodes.
# Architecture and Design Decisions
The decisions below have been made during the writing of this document and shall not be changed.
## Hardware Layer
The bus shall use RS-485 as hardware layer and make use of UART and timer SoC modules available inside micro-controllers.
This allows the use of 3.3V logic level connections for easy testing during early development. Later, RS-485 transceivers can be attached to the development boards.
## Software
Software development shall take place on an open platform.
Initial versions of the implementation may be hardware specific, but the aim shall be to make the lower software layers as hardware independent as possible. Middle and high layers shall be hardware and operating system independent right from the beginning.
One goal for later FieldBus19 implementations is that they are as hardware independent as technically possible. There will be tradeoffs for code and run-time overhead versus generalization of the drivers, but this is a topic for later discussions.
# Next Steps
## Specification Document
A specification document containing the specifications of the FieldBus19 product shall be written. It may evolve as the proof of concept prototype is implemented, but shall be finished with the completion of that project.
## Additional Documentation
Additional documents are optional during proof of concept project phase.
## Proof of Concept Prototype
This prototype shall be implemented on a STM32 based evaluation board.
# Glossary
API	Application Programming Interface
ARCNET	Attached Resource Computer NETwork
ARINC	Aeronautical Radio INC
CAN	Controller Area Network
CPU	Central Processing Unit
CRC	Cyclic Redundancy Check
DIL	Dual In-Line
DMA	Direct Memory Access
IP	Internet Protocol
ISR	Interrupt Service Routine
LAN	Local Area Network
LIN	Local Interconnect Network
OSI	Open Systems Interconnection
PROFIBUS	Process Field Bus
RAM	Random Access Memory
ROM	Read-Only Memory
RS	Recommended Standard
SoC	System on Chip
TCP	Transmission Control Protocol
UART	Universal Asynchronous Receiver Transmitter
UDP	User Datagram Protocol
WLAN	Wireless LAN

# External References
See links above in text sections.