FieldBus19

Description

Version:	1.02

Last Edit:	February 28, 2022

Author:	Andreas Isenegger

Filename:	FB19_Description.odt

Document Revision History

Version	Date	Author	Changes

1.02	28-Feb-2022	A. Isenegger	Chapter Bus Hardware added, paragraph Bus Initialization added, paragraph Bus Modes ’Locked’ and ‘Unlocked’ extended, paragraph CAN vs FieldBus19 added
1.01	19-Dec-2021	A. Isenegger	Applied cosmetic changes to chapter Bus Topology, content added to chapter Frames and Messages
1.00	10-Dec-2021	A. Isenegger	Initial version

Table 1: Document revision history

# Introduction
## Purpose of this Document
This document describes the FieldBus19 field bus and its properties. It is a less formal alternative to the FieldBus19 specification document [1].
## Scope of this Document
TBW
## CAN vs FieldBus19
The FieldBus19 specifications have some similarities to those of the CAN bus. It differs electrically only slightly, however the bus arbitration works differently, and the FieldBus19 integrates higher network layers than the CAN bus does. While CAN requires an IP core on silicon and a driver, FieldBus19 uses UARTs that are found inside almost every micro-controller, and it applies RS-485 transceivers to drive the signals on the bus line. Finally, while the CAN bus is a multi-master bus, the FieldBus19 is a single-master bus.
All this makes the FieldBus19 not a competitor of the CAN bus, but an additional solution from which to choose.
# Definitions
## Bus Nodes
A bus node is a micro-controller on a PCB that is attached to the bus. It performs one of the following bus-related functions:
- Bus Controller
  The bus master. There is exactly 1 active bus master on the bus at any point in time. A bus doesn’t work if there is no Bus Controller connected.
- Backup Bus Controller
  A passive bus master that listens only. It takes over in case the active Bus Controller fails.
  This is an optional component.
- Bus Monitor
  A listen-only bus node that is used for recording, communication supervision and/or fault diagnosis. It doesn't participate in the message exchange and doesn't subscribe to the active Bus Controller. It’s therefore invisible to the all other bus nodes.
  This is an optional component.
- Bus Subscriber
  One to many sensor, actor or other type of units on the bus. Once online after power up, the Bus Controller scans the bus line for attached devices and registers them, thereby establishing communication.
All of the above components execute domain specific tasks of course. For example, the Bus Controller could be a speed controller with speed data as input and power data as output. It might run standalone, or be connected via another bus or a serial connection to a higher level controller entity.
## Frames and Messages
- Bus Character
  A character is one byte of a Bus Frame on the bus line, including its start and stop bits.
- Bus Frame
  A frame is the physical representation of a Bus Message on the bus line.
- Bus Message
  A Bus Message is the logical content of a bus frame. It is the frame’s byte stream as stored inside a micro-controller's memory.
## Bus Initialization
Per definition a bus initialization is a bus reconfiguration after power up of the Bus Controller.
On power up, a Bus Controller may remember if it controlled a bus in its previous life cycle, but it basically has to cope with these situations after power up:
- It's the only bus participant
- It has 1 to 30 Bus Subscribers attached who are
  - All new to this bus (see note below)
  - Some new to this bus, some known to this bus
  - All known to this bus
  - One or more of them electrically or software wise faulty
Note:
In this context, 'new to this bus' may mean that they've been part of another bus in the past and been moved. In this case they recall their bus address after power up, which is most likely wrong.
Alternatively, a new participant may have never been part of a bus system and thus carries the bus address ‘invalid’.
## Bus Modes ’Locked’ and ‘Unlocked’
A FieldBus19 system basically operates in one of two modes: Locked or Unlocked.
In respect of adding or removing nodes to a bus line, the Bus Controller – and subsequently the bus itself – is in one of two modes: ‘locked’, or ‘unlocked’. These modes are mutually exclusive:
- Locked: In this mode, new nodes aren't added to the logical node list inside a Bus Controller since the Bus Controller won't query the bus for new Bus Subscribers. Furthermore, the Bus Controller won't remove unresponsive Bus Subscribers from its list of participants, it will rather mark them as offline as long as they don't respond to messages. In other words, no bus reconfiguration is taking place when a node is added or removed.
- Unlocked: This mode is foreseen for adding or removing nodes from the bus line. When a node is added, the Bus Controller will assign it a bus address, add it to the list of online nodes and start communicating to it. If a node is removed or doesn’t respond for any other reasons to messages from the Bus Controller, it is removed from the Bus Controller’s internal list of nodes. In other words, a bus reconfiguration is taking place when a node is added or removed.
It is the user who decides in what mode a bus is running in. The Domain Application running on the Bus Controller usually contains a user interface that allows the user to select the mode. Client modules of the Bus Controller application can query and change the state of the bus and its participants at any time.
For safety reasons, the Bus Controller is at power up in the ‘locked’ state. Only on user request or because of the corresponding configuration property, it will switch to ‘unlocked’ mode.
## Bus Address
Every node carries a unique bus address. This is a number between 0 and 30. Bus addresses are dynamically assigned by the Bus Controller; no DIL switches or NV memory configuration is necessary for defining a node’s address.
The Bus Controller always has bus address 0.
Bus Subscribers have addresses in the range of 1 to 30. This means that maximum 30 subscriber nodes can be attached to a FieldBus19 system.
If the bus is in ‘unlocked’ mode, the Bus Controller assigns bus addresses at these occasions:
- After power up of the Bus Controller, assuming the Bus Subscriber nodes are already up and running when the Bus Controller powers up
- When a node is electrically attached to the bus
- By user request
- Not part of this list, but good to remember: When a node is removed from the bus or doesn’t respond anymore, it’s address is freed
No address assignment takes place if the bus is in ‘locked’ mode, or if all addresses are in use.
## Unique Node Identifier
Each node on a FieldBus19 system requires a fix and unique identifier, ‘fix’ implying that it’s not changeable by the application, and ‘unique’ meaning that it at least doesn’t exist a second time on that bus system. If any of these requirements aren’t met, frequent frame collisions will be the result, rendering the bus system inoperable.
Many nowadays micro-controller families have a world-wide unique device identifier burnt into their silicon. It’s a very long number that has a read-only register address somewhere in the hardware region of the controller. No other device on this planet has the same identifier. This makes it very well suited for being used as unique node identifier in the context of the FieldBus19.
# Bus Topology
## Physical Topology
The physical transport layer (known as OSI layer 1) is RS-485, also called EIA-485 or TIA-485. This is a half-duplex bus, with high electrical noise immunity and short-circuit protected bus drivers. It’s specified for bit rates up to 10Mbit/s when the bus line is short enough. At lower bit rates it supports cabling in the 100m range. Long cabling requires terminating resistors at the two physical ends, desktop length cabling does not. See Wikipedia for details.
The nodes connect via RS-485 transceiver chips to the bus. They come in various form factors and flavors and are widely available. On the node, the transceiver is wired to the input and output of a U(S)ART module inside the micro-controller.
Bus participants are equipped with one or two bus interfaces. If no redundancy on the physical layer is required, one bus interface per node suffices.
There exist 3 possibilities how to configure a bus hardware-wise:
- All participants including the Bus Controller are connected via 1 bus line; this is the most common application
- Some participants are connected via 1 bus line, some others via 2 bus lines; the Bus Controller is subsequently connected to 2 bus lines
- All participants including the Bus Controller are inter-connected via 2 bus lines
## Logical Topology
Illustration 1: Logical Bus Topology below shows 2 connectors per node, and thus 2 bus lines.

Illustration 1: Logical Bus Topology
The bus specification allows for a logical topology analysis and reflection by the Bus Controller. Note however that it isn’t possible for the Bus Controller to figure out the physical topology of the bus.
# Bus Frames and Messages
A message is the logical entity of an information packet inside a node, while a frame is such a packet on the bus line.
In other words, a frame is the byte array a UART transmitter is sending and its receiver is receiving, while on higher application layers, the software modules or objects pass messages up and down.
## Frame Format
A bus frame is minumum 4 characters and maximum 35 characters long. It has the following format:

Illustration 2: Bus Frame Format
Dst
Addr
Msg
Id
Pld
Size
CS
PD
Char #
1
2
3
PS
+3
PS
+4
PS+2
0 to 31 characters

Fields

Body
Trailer
0
7
7
0
7
0
7
0

High
byte
Low
byte
Header
Fields:
Abbreviation	Full Name	Explanation
DstAddr	Destination Address	5 bits, maximum 32 addresses (1 Controller, 30 Subscribers, broadcast)
MsgId	Message Identifier	6 bits, 0 … 15: FB19 specific messages, 16 … 63: domain specific messages
PldSize	Payload Size	Number of characters in the payload field, 5 bits, 0 … 31 characters
PD	Payload Data	Examples: floating point number (32bit), short integer (16bit)
CS	Checksum	Lower 16bit of the CRC-32 checksum of all bytes inside the frame, except the checksum itself

Notes:
1. This is the frame and byte order as seen on the bus line.
2. The bit order inside a character (byte) on the bus is LSB first (this is the common order for UARTs).
3. Color coding: FB19 specific fields are green, domain specific fields are blue.
4. Frame size: minimum 4 characters, maximum 35 characters.
5. Network byte order for the header and trailer is Big Endian.
6. Network byte order for the body is defined by the domain application.

## Message Format
A message looks similar to a bus frame. It uses 40 bytes of RAM however and all data is in host byte order, which is Little Endian on the STM32F micro-controllers.

Illustration 3: Message Format
Msg
Id
Dst
Addr
Pld
Size
Status

PD
CS
31 bytes

Stuff
Byte

Body
Trailer
Header

Pld
Size
Msg
Id
Dst
Addr

Message Descriptor
Frame
A+0
A+1
A+2
A+3
A+4
A+5
A+6
A+38
A+39

Fields:
Abbreviation	Full Name	Explanation
MsgId	Message Identifier	0 … 15: FB messages, 16 … 63: domain specific messages
DstAddr	Destination Address	32 addresses: 0 is Controller, 1..30 is Subscribers, 31 is Broadcast message
PldSize	Payload Size	Number of characters in the payload field, 5 bits, 0 … 31 characters
Status	Message Status	Status information concerning the message, including reception errors for example
PD	Payload Data	Data to be exchanged between the bus participants
CS	Checksum	Lower 16bit of the CRC-32 checksum of all bytes inside the frame, except the checksum itself
Stuff Byte	Stuff Byte	The stuff byte makes the message object in the RAM 40 bytes long. 40 is divisible by 4, which is optimal for 32bit CPU architectures. The stuff byte makes a message use 2.5% more RAM, but may reduce code in size and execution speed in time.

Notes:
1. 'A' means 'address in RAM'
2. 'A+1' means 'base address in RAM plus 1 byte', 'A+2' means 'base address in RAM plus 2 bytes', and so on
3. The Message Descriptor is a C structure, the Frame is a C array packed into a structure

In C code, a message looks like this:
typedef struct FB19msgDscr_struct
{
    uint8_t msgId; /** Message identifier. */
    uint8_t dstAddr; /** Destination address. */
    uint8_t pldSize; /** Size of the payload data in bytes. */
    uint8_t status; /** Message status bits. */
} FB19msgDscr_t;

typedef struct FB19frame_struct
{
    uint8_t data[FB19_FRAME_SIZE_RAM];
} FB19frame_t;

typedef struct FB19msg_struct
{
    FB19msgDscr_t dscr; /** Message descriptor. */
    FB19frame_t frame; /** Bus frame. */
} FB19msg_t;
## Checksum
Frames are protected against data corruption on the transmission line by the means of a checksum. The STM32F1/2/3/4 micro-controllers offer a hardware CRC unit as SoC module. Since the reference platform is STM32F4 based, it's obvious to choose its CRC type.
The STM32 SoC unit uses the polynomial

X^32 + X^26 + X^23 + X^22 + X^16 + X^12 + X^11 + X^10 +X^8 + X^7 + X^5 + X^4 + X^2 + X^1 + 1

equivalent to 0x1’04C1’1DB7 or 1’0000’0100’1100’0001’0001’1101’1011’0111 in binary form.
This is identical to the CRC-32 Ethernet polynomial. Start value after a reset is 0xFFFF’FFFF.
The advantage of using a hardware unit over a software algorithm is its speed. It requires 4 AHB clock cycles (HCLK) only to compute a new CRC value. The disadvantage is that only this and no other algorithm can be used.
In order to save bandwitdth on the bus line, a checksum inside a frame is only 16 bits long. The lower 16 bits of the 32 bit long checksum are used, the rest is ignored.
# Bus Hardware
TBW
A transmitter wants to see the characters it is sending on the bus line. For this purpose it keeps its receiver switched on during transmission.
# Bus Protocol
TBW
The Bus Controller initiates all bus transactions.
## Static Specifications
TBW
## Dynamic Specifications
TBW

# Glossary
Char	Character
DIL	Dual In-Line
EIA	Electronic Industries Alliance
FB19	FieldBus19
LSB	Least Significant Bit
NV	Non-Volatile
OSI	Open System Interconnect, a network layer specification
PCB	Printed Circuit Board
RAM	Random Access Memory
RS	Recommended Standard
SoC	System on Chip
TBW	To Be Written
TIA	Telecommunication Industries Association
U(S)ART	Universal (Synchronous and) Asynchronous Receiver and Transmitter, a SoC	module inside a micro-controller for serial communication
# External References
[1] FieldBus19 Specifications
Filename: FB19_Specifications.odt