FieldBus19

Description

Version:	1.00

Last Edit:	December 10, 2021

Author:	Andreas Isenegger

Filename:	FB19_Description.odt

Document Revision History

Version	Date	Author	Changes

1.00	10-Dec-2021	A. Isenegger	Initial version

Table 1: Document revision history

# Introduction
## Purpose of this Document
This document describes the FieldBus19 field bus and its properties. It is a less formal alternative to the FieldBus19 specification document [1], but references it where necessary.
## Scope of this Document

# Definitions
## Bus Nodes
A bus node is a micro-controller on a PCB that is attached to the bus. It performs one of the following bus-related functions:
- Bus Controller
  The bus master. There is exactly 1 active bus master on the bus at any point in time. A bus doesn’t work if there is no Bus Controller connected.
- Backup Bus Controller
  A passive bus master that listens only. It takes over in case the active Bus Controller fails.
  This is an optional component.
- Bus Monitor
  A listen-only bus node that is used for recording, communication supervision and/or fault diagnosis. It doesn't participate in the message exchange and doesn't subscribe to the active Bus Controller. It’s therefore invisible to the all other bus nodes.
  This is an optional component.
- Bus Subscriber
  One to many sensor, actor or other type of units on the bus. Once online after power up, the Bus Controller scans the bus line for attached devices and registers them, thereby establishing communication.
All of the above components execute domain specific tasks of course. For example, the Bus Controller could be a speed controller with speed data as input and power data as output. It might run standalone, or be connected via another bus or a serial connection to a higher level controller entity.
## Frames and Messages
- Bus Character
  A character is one byte of a Bus Frame on the bus line, including its start and stop bits.
- Bus Frame
  A frame is the physical representation of a Bus Message on the bus line.
- Bus Message
  A Bus Message is the logical content of a bus frame. It is the frame’s byte stream as stored inside a micro-controller's memory.
## Bus Modes ’Locked’ and ‘Unlocked’
In respect of adding or removing nodes to a bus line, the Bus Controller – and subsequently the bus itself – is in one of two modes: ‘locked’, or ‘unlocked’. These are two mutually exclusive states:
- Locked: In this mode, new nodes aren't added to the logical node list inside a Bus Controller, and removed nodes (or those not responding anymore) are internally marked as offline, but not removed from the list of nodes. In other words, no bus reconfiguration is performed when nodes are added or removed.
- Unlocked: This mode is foreseen for adding or removing nodes from the bus line. When a node is added, the Bus Controller will assign it a bus address, add it to the list of online nodes and start communicating to it. If a node is removed or doesn’t respond for any other reasons to messages from the Bus Controller, it is removed from the Bus Controller’s internal list of nodes. In other words, a bus reconfiguration is taking place when a node is added or removed.
For safety reasons, the Bus Controller is at power up in the ‘locked’ state. Only on user request or because of the corresponding configuration property, it will switch to ‘unlocked’ mode.
Clients of the Bus Controller application can query the state of the bus and its participants at any time.
## Bus Address
Every node carries a unique bus address. This is a number between 0 and 30. Bus addresses are dynamically assigned by the Bus Controller; no DIL switches or NV memory configuration is necessary for defining a node’s address.
The Bus Controller always has bus address 0.
Bus Subscribers have addresses in the range of 1 to 30. This means that maximum 30 subscriber nodes can be attached to a FieldBus19 system.
If the bus is in ‘unlocked’ mode, the Bus Controller assigns bus addresses at these occasions:
- After power up of the Bus Controller, assuming the Bus Subscriber nodes are already up and running when the Bus Controller powers up
- When a node is electrically attached to the bus
- By user request
- Not part of this list, but good to remember: When a node is removed from the bus or doesn’t respond anymore, it’s address is freed
No address assignment takes place if the bus is in ‘locked’ mode, or if all addresses are in use.
## Unique Node Identifier
Each node on a FieldBus19 system requires a fix and unique identifier, ‘fix’ implying that it’s not changeable by the application, and ‘unique’ meaning that it at least doesn’t exist a second time on that bus system. If any of these requirements aren’t met, frequent frame collisions will be the result, rendering the bus system inoperable.
Many nowadays micro-controller families have a world-wide unique device identifier burnt into their silicon. It’s a very long number that has a read-only register address somewhere in the hardware region of the controller. No other device on this planet has the same identifier. This makes it very well suited for being used as unique node identifier in the context of the FieldBus19.
# Bus Topology
## Physical Topology
The physical transport layer (known as OSI layer 1) is RS-485, also called EIA-485 or TIA-485. This is a half-duplex bus, with high electrical noise immunity and short-circuit protected bus drivers. It’s specified for bit rates up to 10Mbit/s when the bus line is short enough. At lower bit rates it supports cabling in the 100m range. Long cabling requires terminating resistors at the two physical ends, desktop length cabling does not.
The nodes connect via RS-485 transceiver chips to the bus. They come in various form factors and flavors and are widely available. On the node, the transceiver is wired to the input and output of a U(S)ART module inside the micro-controller.
Bus participants are equipped with one or two bus interfaces. If no redundancy on the physical layer is required, one bus interface per node suffices.
There exist 3 possibilities how to configure a bus hardware-wise:
- All participants including the Bus Controller are connected via 1 bus line; this is the most common application
- Some participants are connected via 1 bus line, some others via 2 bus lines; the Bus Controller is subsequently connected to 2 bus lines
- All participants including the Bus Controller are inter-connected via 2 bus lines
## Logical Topology
Illustration 1: Logical Bus Topology below shows 2 connectors per node, and thus 2 bus lines.

Illustration 1: Logical Bus Topology
The bus specification allows for a logical topology analysis and reflection by the Bus Controller. Note however that it isn’t possible for the Bus Controller to figure out the physical bus topology of the bus.
# Frames and Messages
TBW
The difference between a frame and a message is ...
## Format
TBW
## Checksum
TBW

# Bus Protocol
TBW
The Bus Controller initiates all bus transactions.
## Static Specifications
TBW
## Dynamic Specifications
TBW

# Glossary
DIL	Dual In-Line
EIA	Electronic Industries Alliance
NV	Non-Volatile
OSI	Open System Interconnect, a network layer specification
PCB	Printed Circuit Board
RS	Recommended Standard
SoC	System on Chip
TBW	To Be Written
TIA	Telecommunication Industries Association
U(S)ART	Universal (Synchronous and) Asynchronous Receiver and Transmitter, a SoC	module inside a micro-controller for serial communication
# External References
[1] FieldBus19 Specifications
Filename: FB19_Specifications.odt