FieldBus19

Specifications

Version:	1.00

Last Edit:	December 8, 2021

Author:	Andreas Isenegger

Filename:	FB19_Specifications.odt

Document Revision History

Version	Date	Author	Changes

1.00	08-Dec-2021	A. Isenegger	Initial version

Table 1: Document revision history

# Introduction
## Purpose of this Document

## Scope of this Document

# Overview
## Communication Fault Types
### Bus Controller
While receiving:
Error	Detector	Time of detection	Cause(s)	Action(s)
CRC Error	drvFB19Ctrl _readMsg() -> unpack() -> calcChecksum()	When message is read by dprFB19Ctrl.handler() from drvFB19Ctrl	Flipped bit(s) on the bus line due to electrical distortion or frame collisions	Discard message, ignore contents
Character Framing Error (USART_SR_FE)	USART receiver	At the end of a character reception	The receiver line doesn’t go high after a Stop bit	Discard message, ignore contents
Character Noise Error (USART_SR_NE)	USART receiver	During character reception	The bus line is unstable during the bits inside a character	Discard message, ignore contents
Receive Data Register Overrun Error (USART_SR_ORE)	USART receiver	At the end of a character reception	The receive data register hasn’t been read before the next character has been received	Discard message, ignore contents

While transmitting:
Error	Detector	Time of detection	Cause(s)	Action(s)
Rx char != Tx char	drvFB19UART -> ISR	When the ISR is called because the transmit data register is empty	Electrical distortion on the bus line or a collision of frames	Abort transmission of frame immediately
Character Noise Error (USART_SR_NE)	USART receiver	During character transmission; the USART is simultaneously receiving what it is transmitting	The bus line is unstable during the bits inside a character	Abort transmission of frame immediately

### Bus Subscriber
While receiving:
// TODO 2021-12-08 To be formatted

- CRC error
  - Is detected when message is read from drvFB19Subs:
    drvFB19Subs_readMsg() -> unpack() -> calculateChecksum()
- USART_SR_FE
  - Detected by UART when line doesn't go high after Stop bit
- USART_SR_NE
  - Detected by UART when line is instable during the bits inside a character
- USART_SR_ORE
  - Detected by UART when receiver overwrites data register before it has been read

While transmitting:
- Rx char is != Tx char
  - This is either a strong electrical distortion on the signal lines, or a collision of frames because two or more nodes are transmitting simultaneously

# Glossary
!=	Not equal to
char	Character: a data byte on the bus line, including start and stop bits
CRC	Cyclic Redundancy Check
ISR	Interrupt Service Routine
USART	Universal Synchronous/Asynchronous Receiver and Transmitter
# External References
[1] FieldBus19 Requirements
Filename: FB19_Requirements.odt